## Slide 1
Sub-Scale Judder Testing: Correlating a Bench Machine with the Vehicle
A methodology for classifying clutch facing judder sensitivity on a sub-scale bench test instead of a full vehicle, with preliminary results showing good correlation to the car.

## Slide 2
⏱️ The problem
Today the judder test is performed in a car that is known to be sensitive to judder. The test itself is valid, but it is expensive in time: a complete clutch set — disc, clutch cover and flywheel — has to be assembled for every single test.In a material development programme where dozens of formulations are screened, that assembly time dominates the schedule.

## Slide 3
🔬 The approach
This work develops a methodology to classify facing sensitivity to judder on a sub-scale bench test rather than in the vehicle. The goal is explicitly twofold: cut the time each test takes, and speed up friction material development as a whole by allowing more candidates to be screened.Sub-scale means the test article is smaller than a production facing, which is what removes the full clutch-set assembly from the loop. The open question is whether a smaller sample, tested on a bench, still ranks materials the same way a car does.ℹ️Correlation — not the raw numbers — is what determines whether a bench test can genuinely replace vehicle time.

## Slide 4
📊 What came out of it
The preliminary results are described as very promising, because of a good correlation between the sub-scale tests and the vehicle. Correlation is the load-bearing word here — a bench test that produces numbers is easy, while a bench test that produces the same ranking as the car is the thing that actually replaces vehicle time.

## Slide 5
💡 Why it matters
Screening on a sub-scale machine changes the economics of judder work. Candidates that would never have justified a vehicle test can be evaluated, and the vehicle is reserved for confirming the shortlist rather than discovering it.

## Slide 6
📄 Full publication
Gregori, I. R. S.; Haertel Jr., W. — Judder based on Sub Scale Test Machine Concerning Facing. SAE Technical Papers, April 2013.Read the full publication on ResearchGate